## Slide 1: Silicon VME Crate 2k
Power PC
Event Manager Slave
VME 60 MB/s
Main data stream to Event Builder
4MB/s
Event # from Event Manager
RACEway
160 MB/s
Si VME Crate
Configuration for Run 2000

## Slide 2: Phobos DAQ 2k1 Phase 1
Scalers
Power PC
Event Manager
L0
L1
RACEway
160 MB/s
Logical Disk 1
4*18 GB
Logical Disk 0
4*18 GB
Gigabit to RCF
SCSI
40 MB/s
Event # to TOF+
The disk array is fully operational. The aggregate write/read performance = 40+40 MB/s
Disk Array (RAID0)
Data from TOF+
VME 80MB/s
Advantage
Minimal changes in software
Disadvantages:
Heavy traffic on USP 40+40+40+40 MB/s
Sophisticated Event Building
Synchronization required
USP
Ultra SPARC
Gigabit Interface is in place. Driver is not installed yet.
SCSI
40 MB/s
4 boards are in use.
1 board has a problem
5 spare boards fully assembled
Data from Silicon detectors
60 MB/s
RACEway processor farm:
10 PowerPC-604/750 300 MHz
Backplane crossbar switch 600 MB/s aggregate bandwidth.
2 Data Input channels 60 MB/s
VME Crate (silicon)

## Slide 3: Phobos DAQ 2k1
Scalers
PowerPC
for VME processing
Event Manager
L0
L1
USP
Ultra SPARC
Data mover
Gigabit to RCF
SCSI
40 MB/s
Achieved
35 MB/s
SCSI
40 MB/s
Achieved
18 MB/s
Event # to TOF+
SUN Ultra 300 or second USP
Logical Disk 1
4*18 GB
Logical Disk 0
4*18 GB
Local
Ethernet
Data from TOF+
Not tested
Advantages:
Reduced I/O traffic on USP 40+40 MB/s
Simplified Event Building
No synchronization required
No Gigabit on VME
Simplified pipelining
Disadvantage
Need to “simplify” software
RACEway
160 MB/s
Data from Silicon detectors
60 MB/s
Disk Array (RAID0)
RACEway processor farm:
24 PowerPC-750 300 MHz
Backplane crossbar switch 600 MB/s aggregate bandwidth.
2 Data Input channels 60 MB/s
The rest 14 CPUs scheduled for delivery in December 2000.
Si VME Crate
SPARC-RACEway Interface exists. Driver should be available shortly

## Slide 4: Compression
Conclusion:
Compression using Huffman coding on Mercury is doable. It is not sensitive to the data dispersion.
The achievable compression factor (relative to the run 2000) is 1/(0.70*0.70*12/16) = 2.7

## Slide 5: Pedestal Suppression
Gains
Histogramming chip based
Find median
Remove dead channels
CMN correction
Pede-
stals
Subtract median
Above RMS
?
Suppression
enabled?
Ped
RMS
Output data
Input data
Using current Phat method is possible but it is slightly slower
Features:
For non suppressed data it is possible to retrieve raw value
Pedestals are subtracted for all detectors
CMN are subtracted for all detectors
Data suppression is done only for spectrometer
Yes

## Slide 6: Si Data Format (Draft)

## Slide 7: I/O performance
Measured performance using disk bench program bonnie for simultaneous writing/reading
Configuration:
USPII->SCSI(40MB/s)->RAID
RAID->SCSI(20MB/s)->Ultra3000
Performance:
Writing channel: 33 MB/s, CPU usage = 50%
Reading channel: 16 MB/s, CPU usage = 20%
File system configuration
RAID controller allocates separate SCSI ID numbers for both logical drives on both host channels.
Writer host (USPII, vmesparc) have both logical drives mounted with read/write option.
Reader host (Ultra3000, phobosx) have the same logical drives mounted with read only option (required to keep the file system consistent).
To get updated directory info on the shared drives the reader should remount the drive.