## Slide 1: DAQ Bottlenecks
Silicon to Mercury. 700 ev/s, 200 MB/s, based on single event data taking time = 1.4 ms
Mercury to UltraSPARC. (hard 80 MB/s, soft 64 MB/s) test program: 520 ev/s, 52 MB/s, 40% CPU
UltraSPARC to disk. 447 ev/s, 44.7 MB/s, 4% CPU test program.
Mercury to disk. 230 ev/s, 23 MB/s, 50% CPU test program. There is a room for improvement.
Disk to RCF. 250 ev/s, 25-30 MB/s test program.
Silicon to disk. ?, working on it…

## Slide 2
Additional hardware:
FPDP-PMC interface, $2k
ROUT PMC board, $2k
Dual SCSI-PCI interface, $1k
PCI-Gigabit interface, $1k
Disk enclosure, $2.5k
4*180 GB disks, $8k
Advantages:
Known parts.
Disadvantages:
Ultra 5 will be overloaded. Upgrading to double CPU will cost $15k

## Slide 3
Additional hardware:
Fiber channel - RACEway, $6k?
Fiber channel RAID controller, $4.4k
Fiber channel HBA, $2k?
PCI-Gigabit interface, $1k?
Advantages:
Mercury to disk directly @100 MB/s
Disadvantages:
No file systems on the disk array. How to PFTP to RCF?
All data should be available in Mercury.