## Slide 1: Achieved
Compression performance = 14 MB/s/CPU
Data taking time in Mercury for 2 events = 5.1 ms. Instantaneous data taking rate in Mercury = 400 Hz.
Sustained rate in Mercury 300 Hz. After fixing a bug it is expected to be 400 Hz.
Data taking with writing = 180 Hz, 19 MB/s. At this rate the vmesparc was 60% busy, disk was 50% busy.
FPDP Link from Mercury to UltraSPARC = 40 MB/s
Writing to the disk using test program = 50 MB/s
Sending to the RCF = 25-30 MB/s

## Slide 2: Estimation of the Maximum DAQ rate
For PP data we can expect compression factor 4.5, the event size = 295 KB/4.5 = 66 KB. At 900 Hz it correspond to 59 MB/s. Disk array with new vmesparc with 80 MB/s SCSI should handle this rate.
It is possible to distribute data evenly between 21 CPU so that the maximum data size = 14432 bytes
Data in 14 kB / 160 MB/s | 90 s
Processing 14 kB / 14 MB/s | 1000 s
Data out 4 kB / 160 MB/s | 25 s
Total | 1115 s
The following table shows itemized busy time of a single worker.

## Slide 3: Distribution of FECs between workers
This table shows the optimal distribution of FECs between 21 workers. Amazingly the number 21 is optimal for our setup, it allows maximal size of the worker = 14336 bytes. The next magic number of workers is 25, it has max worker size = 13312 bytes. To get the max worker size minimal (but full FECs) one need 32 workers and max worker size will be 12288.