## Slide 1: Silicon Front End Electronics and Data Acquisition System for PHOBOS experiment at RHIC
Silicon Front End Electronics and Data Acquisition System for PHOBOS experiment at RHIC
Pradeep Sarin for PHOBOS Collaboration
October 05 2000
Fall 2000 DNP Meeting

## Slide 2: Plan
Description of Silicon Detectors/FEE : (Silicon modules + Viking + FEC = 2 slides )
Description of Data path : (DMU + MDC + Mercury RACEway + Solaris Host)
Description of Trigger Management : (Event Manager and Trigger Managers)
Performance description: (Si Front-end Noise and stability, Data rates)

## Slide 3
PHOBOS Experimental Setup
Silicon Pad detectors for measuring charged particles (Multiplicity and Tracking/PID) + Plastic Scintillator for Triggering and TOF
137,000 Silicon Readout Channels
1,300 Scintillator Readout Channels
Nominal Interaction Point

## Slide 4
Run 5332 Event 35225 08/31/00 06:59:24 PHOBOS Online Event Display
Spectrometer Arm N
Spectrometer Arm P
Octagon Multiplicity
detector
Trigger
Scintillators N
Trigger
Scintillators P
Not to scale
Not all sub-detectors shown
Au-Au Beam Momentum = 65.12 GeV/c

## Slide 5
PHOBOS Readout Scheme
Silicon Detector Modules
Front End Controllers
Silicon Pad detectors
~1500 pads
IDE VA and
VA - HDR1
Readout Chips
ANALOG
Data Multiplexer Unit
Mercury RACEway/VME
Zero Suppression System
DIGITAL G-LINK
FIBRE-OPTIC
Event Builder
DISKS
100Mbps UDP
Trigger Detectors TOF array
LeCroy FASTBUS
ADC + TDC modules
VME+NIM based
Trigger
Management
100Mbps UDP
100Mbps UDP
ANALOG
L0, L1 TRIGGER

## Slide 6
Silicon Front End Electronics
Double Metal, Single sided, AC coupled,
polysilicon biased detectors
produced by ERSO, Taiwan
VA and VA-HDR1 readout Chips
produced by IDE AS
1.2 s peaking time
Radiation tolerance to ~ 20 kRad
Low Noise (~ 900 ENC/pF)
Dynamic Range ~ 100 MIPs
VA Biasing and Triggering
VA Signal readout
and digitization
12-bit ADC (ADS802)
VA Calibration
Xilinx FPGA
Controller
VA Monitoring
G-LINK Output
Trigger
Front End Controllers designed and produced by MIT-LNS Electronics Facility (Bernie Wadsworth Group)
Low Noise (~ 450 ENC/pF)
NO measurable CMN introduced in signal path
Each FEC controls upto 6K readout channels
50 MB/s output and double Event buffering
Specialized monitoring of VA supply lines to detect radiation induced latchup
PREAMP
SHAPER
OUTBUF
FEC
p+ Implant
n+
Polysilicon
Drain Resistor
bias bus
signal lines
vias
0.2um ONO
1.2um ONO
300 m 5k nSi

## Slide 7
MVME 2306
MVME 2600
MVME 2306
GigaEthernet
to RHIC computing Facility
GigaEthernet
CPU
CPU
4 CPU
Local Disc
Tape
Fast
Ethernet
Trigger VME
FastEthernet
SUN HPC 3000
Event Manager
TOF+TRIG FASTBUS
ADC
TDC
Trig ADC
Trig TDC
SFI
340
RACEway
RACEway
RACEway
RACEway
Silicon VME
Event Manager
Event Manager
L0 Manager
L1 Manager
Event Builder
software in ROOT framework
Multiplexed Data in from Silicon FEC’s
Data in from TOF/Trigger modules
Triggers in from Trigger detectors
Data Acquistion System
Online System
ROOT framework

## Slide 8
Worker 1 CN
Worker 2 CN
RAM
Master CN
L1/ L2 Trigger
Event #
Send Command Words and Event Tag to MDC.
Disable Trigger.
Synchronize the Worker CN’s by sending Event info
Receive ACK from all Worker CNs for receipt of data for event
Enable L2 trigger
RAM
Worker n CN
Send ACK to Master CN.
Pedestal Subtraction
Pedestal
+ GAIN data for Group of FECs
Zero Suppression
Common Mode Noise Correction?
Send Size of ZSS data to Master CN
Collect all packets of Zero Suppressed data and join them together.
+
+
+
Write Zero Suppressed Events to VxWorks Host.
RACEway transfer (DMA)
~ 140MB/s
VME BackPlane ~ 80 MB/s
MVME 2604 Interface to
Event Builder
RAM
VxWorks
RIN-T (FIFOs)
Raw Event Data
from FEC
ROUT (FIFOs)
ZSS
Event Loop in Silicon DAQ

## Slide 9
Trigger Management
Boards designed by Andrei Sukhanov (BNL,PHOBOS)
One design based on Lattice ispLSI3328 PLD
Used with different firmware for separate applications
VME compliant, with dECL inputs
Level 0, Level 1 Trigger Managers: - Implement trigger logic in different modes - Set BUSY signals using inputs from subsystems - Allow software configured pre-scaling and selection of trigger types
Event Manager Master and Slave boards - Master resides in Trigger VME crate, slaves in other sub-system crates - Provides reliable synchronization between sub-systems : strobes out Event Numbers for accepted triggers - Final event-building relies on these synchronized Event numbers.
Master Event Manager
Level 1 Manager
Level 0 Manager
Slave Event Manager
Slave Event Manager
Trigger from Trigger Detectors
Event #
Event #
Trigger + Event # to
Silicon Front End
Trigger + Event # to
Plastic Front End

## Slide 10
Performance in Physics Run 2000
RHIC delivered ~2.7 b-1 integrated luminosity to PHOBOS over 6 weeks of running in Summer 2000.
Silicon systems performed to specifications : Average S/N measured in the detector was 15 to 20 depending on Sensor type. 98% channels fully functional.
Front End Electronics were stable. Every instance of latch-up in the VA chips was detected successfully during adverse beam conditions.
PHOBOS captured ~3.5M events on tape : mixture of minimum bias and central triggers. 99% DAQ uptime.
Sustained data throughput rates of 5MB/s for Event-Builder writing events to local disk.

## Slide 11
Planned Upgrades for 2001 Run
RHIC will increase luminosity by a factor of 10
Second Arm of Spectrometer will be installed  40K more readout channels
Event Builder will be moved from Sun workstation into VME based UltraSPARC server with local RAID disks. Projected increase of throughput rate to ~ 20 MB/s