## Slide 1: Cross Talks Everywhere
Andrei Sukhanov – measurements, analysis
Ioury Sedykh – software, calculations
Piotr Kulinich – measurements, critique
T0 cabling and signals
Cross talks between twinax cables?
Noise in the tunnel
What can be done?
New front-end electronics

## Slide 2: T0 cables
TEQ
ECL
NIM
NIM
ECL
TDC
17
SpectraStrip 15 ns
Twinax 200 ns
Coax 100 ns
SpectraStrip 10 ns
LE
Disc
VME
TDC
TAC
Pulse at ECL/NIM. Using twisted pair cables
Pulse at ECL/NIM. Using twinax cables
The rise time is 5 times shorter
SpectraStrip 60 ns

## Slide 3: Cross talk in rolled twisted pair delay cable
T0N vs T0P on FB TDC08, twisted pair delay cable
T0N vs T0P on FB TDC17, coaxial delay cable
If the time difference between signals on the neighboring channels is less than the rise time on the receiving end, then the signals will be shifted in time due to a cross talk.

## Slide 4: Cross talk between twinax cables. Time Calibrator run
T0P0 vs T0N. The horizontal shifts in 3 spots on the right are due to different contribution from individual P0N channels to the T0N OR, this is acceptable. The vertical shift for lower spot is also acceptable. The problem is with the vertical shift between upper spot and 3 right spots. The same conditions on T0P but changing something on T0N causes shifts in T0P0. The common rule: the signal which comes later gets bigger shift.
The TDC reading of the individual T0P0 channel (twinax + ribbon + ECL/NIM) depends on which channels are enabled in the T0N.
Discriminators are OK.
Time Equalizers are OK.

## Slide 5: Cross talk between ‘twinax’ cables in SPECTOF run
T0N vs T0P. Time in ns. The diagonal stripe – enhancement due to the SpecTOF trigger
OctDeVtx.vz [mm] vs. T0N-T0P [ns]
OctDeVtx.vz [mm] vs. T0N-T0P [cm] Using individual T0 channels
The T0_OR vertex is non-linear relative to the Octagon vertex position

## Slide 6: Correlation between TAC and T0N-T0P
T0 TAC vs T0N-T0P [ns]. Perfectly correlated in all files later than 12069+.
The chain ECL/NIM - coax 100 ns – NIM/ECL – twisted pair 10 ns is OK.
VME TDCs. The distortion from the straight line is due to the cross talk in the 60 ns rolled ribbon cable.
T0 TAC vs T0N-T0P [30ps] using VME TDCs. The same shape in all files.

## Slide 7: Cross talk summary
The time shifts of the signals on the neighboring channels occur when the signals have overlapping edges on the receiving end.
The SpectraStrip twisted pair cables should be avoided in the time measurements.
Using twinax cable the rising/falling time is 5 times shorter than with twisted pair cables. The cross talk is also significantly smaller. We should expect the time shifts at least 20 time smaller.
The observed time shifts in neighboring channels in ‘twinax’ cables are still significant ~ 300 ps.
This shift could probably be eliminated by proper cable grounding, better routing in the counting house.

## Slide 8: Noise in the tunnel
Ground noise on T0P0 (ch1) and T0N0 (ch 2). Both signals have peak-to-peak amplitude 6 mV, the T0P0 have positive offset 4 mV.
T0P0 (ch1) vs T0N0 (ch2)
In Pr03 run there are stable correlations between the noises in different points of the PHOBOS. The amplitude changes depending on beam conditions.
In Run Pr02 there was no such correlations.
Correlations between pedestals of the different ADC channels.

## Slide 9: Scenarios
Unrealistic scenarios:
Replace all cables with twinax. ~ 60 K$. A lot of work
Separate signals in time (~20 ns). Impossible. A lot of work.
Move FASTBUS into the tunnel. Almost no advantage: - Need a remote controlled logic for self-triggering inside the tunnel - Still need ~ 100 ns of cable delays due to the Common Start. - Need very reliable Fast Clear
Realistic scenarios:
Replace only T0 cables.
Replace Front End electronics. ~ 60 K$. Can be done by Nov 1.

## Slide 10: Replace Fastbus with modern readout electronics
SLVME - Optical S-link to VME interface
high speed full duplex S-link optical connection (128 Mbyte/s S-link to PCI and 500 Kbit/s PCI to S-link)
L1 Trigger Strobe Optical Input(FanOut via private bus)
L2 Trigger Word optical TAXI reciever(FanOut via VME broadcast)
Timing/Control ECL Inputs(FanOut via private bus)
Model: NA48 KABES (KAOn Beam Spectrometer) READ-OUT System http://afi.jinr.ru/kabes/

## Slide 11: ROC- Read Out Card
Existing: ROC – KABES
48 TDCs channels 100 ps (measurement of leading and trailing edges)
6 HPTDC chips
L2 64 KByte on-board L2 Ring buffer
Built-in test capabilities
Xilinx Virtex-II - main logic
Proposed: ROC - PHOBOS
Replaces 48 TDC and 48 ADC Fastbus channels
48 TDCs channels (measurement of leading edge with 25 ps resolution and trailing edge with 100 ps )
TOT technique gives information about signal amplitude for slewing correction
6+1 HPTDC chips

## Slide 12: Advantages/Disadvantages
Advantages:
Dead-time-free triggering
No delay cables
Simultaneous Time (25 ps) and Amplitude (TOT) measurement
FPGA on board. Possible decisions for L2: energy deposition in clusters etc.
Cross-talk is not detectable.
The system (100 ps) is fully tested and now is running in the KABES at NA48
Disadvantages:
For amplitude measurements the existing LE discriminators need to be replaced by Philips (55 available in HEEP)