## Slide 1: DAQ Upgrade 04

## Slide 2: What We Have
Current parameters
Fully pipelined system (Except Silicon)
Accepted triggers rate: 230 ev/s
Dead time: fixed 4 ms
Writing to disk: 25 MB/s
FPDP from Mercury to host: 40 MB/s
Sinking to HPSS: 22 MB/s
Demonstrated limits
Max. raw writing to disk: 50 MB/s
From Mercury to host: 40 MB/s
From Mercury to host: 400 ev/s
Competing

## Slide 3: What need to be done
Improve reliability and performance of the FASTBUS. - Transfer directly to the Mercury crate - Multi-event
Improve reliability of the Silicon readout at higher rates.
Satisfy Nigel and Gabor. Accept most of the high-selectivity triggers but fill the rest of the time with the minimum bias events. Not an easy task.

## Slide 4: Upgrade
Silicon
FrontEnd
Mercury
FPDP
FPDP
VME
Sun
Sun
GigaBit
HPSS
FPDP
TK 200
GigaBit
HPSS
No modifications in the data collecting subsystems
Phase out the Sun: ultrasparc and phobosx
Dedicated data recorder instead of a general purpose workstations
Gigabit Ethernet from Linux to HPSS.
Goal
Accepted triggers rate: 500 Hz, 50 MB/s
Dead time: 1.4 ms
Bottleneck: Silicon @ 800 Hz

## Slide 5: Big River TK200 from Conduant

## Slide 6: TK200
Big River TK200 Specifications
Max. Data Rate 200 Mbytes/sec ~ sustained
Max. Disk Drives (16) EIDE ATA 100, packaged in easily removable drive modules. Total 3.2 TB.
Two Gigabit Ethernet ports
Max. Duration 24/7 recording in Pendulum mode (addt'l modules required)
External Interface Front Panel Data Port (FPDP) ~ 50MHz at 32-bit
Power ATX 550W
Chassis Dimensions (5U) 9”H x 19”W x 26”D Rackmount
Operating Systems Windows NT/200/XP, Linux
Used in:
MIT - Haystack Observatory Mark 5 VLBI Data System

## Slide 7: Schedule