## Slide 1: DAQ Status
Recorded input rate 80 Hz. Instantaneous rate ~ 400 Hz (during 0.1 s), sustained: 160 Hz. Problem at the rate above 200 Hz: Does not handle properly the Event Builder overflow.
Data taking times: `Silicon: 1.8(1.4) ms . Fastbus: 2.0 ms. VME: 1.0 ms.
Correct synchronization between Silicon, Fastbus and VME
All L0, L1 bits are in the data stream.
Compression factor 3.3 (9800 ev/seq)

## Slide 2: DAQ Problems & Plans
Handling of the Event Builder Overflow on UltraSparc.
Stop/Start run.
Unexpected L0. Rare, resulting in the Fastbus mismatch. Recoverable during data taking.
Fastbus ADC 18, 22. Several per sequence.
Spectrig TDCs. Needs commissioning.
Corrupted events. Workaround for offline by Burt.
Minor memory leak in the TPhDAQFile.