## Slide 1: Event Builder for Phobos
Subsystem Average Maximum Note
Silicon 30 KB 300 KB Occasional uncompressed (300k) event
TOF+Trig 2 KB 8 KB

## Slide 2: Event Building in CODA
Token: Batch of fixed number of events prepared for sending over the network
Token frequency: 0.1 Hz
ROC bandwidth: 10 MB/S
Token memory 1MB
Multiple buffering > 2
Max/Average event size 10
Total ROC buffer memory 20 MB
Average event size 30 KB
Token size 40 events

## Slide 3: ROC-EB Synchronization. (preliminary)
One of the ROCs is a master. It is equipped with VME output register. All other ROCs equipped with VME input register. Master ROC distribute event number and, possibly, event type via cable connection between registers.
All ROCs receives L2 trigger and starts conversion.
Master ROC waits until it has a room for N events (N should be greater than the maximum event FIFO depth in the system).
Master ROC increments event number and distribute it to other ROCs,
Other ROCs, before putting subevent into the CODA buffer should wait for the increment of the event number.
ROC should put the subevent into the CODA buffer after detecting this increment, if it has no data to send, it should put an event header.
If ROC has a full token, it sends it to the EB.
If EB detects a mismatch between subevents from different ROCs, it forces the master ROC to hold the event number for a time interval, long enough to free all FIFOs and mark next event type as a sync.

## Slide 4: Data Magazine
Autonomous time 3h
EB output bandwidth: 10 MB/S
Disk writing speed: 7.5 MB/S
Total 100 GB 75 GB
Ultra Wide SCSI bandwidth 40 MB/S
Disk data transfer 12 MB/S
Measured writing speed 7 MB/S
The expensive RAID is not necessary.
We can do simultaneous writing/reading with
7 MB/S. This meet our requirements.
We need only additional disks (100$/GB)

## Slide 5: Experience with CODA
Advantages
Source available
Distributed error/status logger CMLOG
Downloadable object code for ROC
Components (ROC,EB,RunServer) have similar structure(tcl/tk shell) and communication protocol (DP)
Interface to Slow Control (EPICS)
Support FASTBUS, VME
Distributed data servise (DD)
Run control database (MSQL)
Long time on line
Prompt user support
Disadvantages
Mess with documentation
Complexity
Unexpectedly low network performance. 5MB/S instead of 10
Special trigger electronics

## Slide 6: DAQ Performance

## Slide 7: Current Status
We have got all required PowerPC processor boards. Three of them have Fast Ethernet (one MVME2306 at BNL, one MVME2306 at Rochester and one MVME2604 with MPMC202 PMC).
The SUN HPC server equipped with
Quad Ethernet NIC with all necessary software
2 UltraSparc CPU, each of them rated as 65 rootmarks
4.2 GB internal disk with sustained rate 12.5 MB/sec. Free slots for additional 9 disks. All disks are connected to single Ultra Wide SCSI controller.
Backup DAT tape 1MB/sec.
The CODA software is installed on the server and MVM2306. The transfer rate between MVME2306 and the server for short events of 40Kbyte length is 5MB/sec.

## Slide 8: Needs
GigaEthernet NIC from ALTEON (price = 1700$). This was recommendation from the RCF group.
Jumbo frame software for ALTEON, which makes it possible to reduce processor load by factor of 2. (price = 700$)
The event storage for 3 hour run at 10MB/sec requires 100 GB of disk space. We don’t need expensive RAID. Just to feel server’s tray with 9/18 GB disks. Price is 100$/GB
We shell consider to add 2 more CPU (price for CPU board with 2 processors is 6000$).
For connection of the subsystems to the Slow Control system it will be required some devices like Scanning Digital Multimeter, any GPIB devices, any serial devices and a 1458 Arcnet Mainframe.