## Slide 1: Event Builder performance
Notes:
The server is SUN Ultra300 with 2 CPU (250 Mhz, 4MB Cache, UltraSPARC), 256 MB of memory , 4.2 GB 7200 RPM Wide Ultra SCSI disk.
CPU_sec is a 1 sec execution on single 250 Mhz UltraSPARC CPU
RT_sec is 1 sec of real time on the server
The data was generated by event simulator running on the second CPU and sending data via UDP socket (as real ROC should do).
The red KB/RT_sec curves are saturated due to the limited performance of the event simulator, the blue curves - due to the disk throughput.
Conclusion:
For event size between 8 and 16 KB the writing performance is 6-8 MB/sec, one CPU is completely busy. The difference between ‘simple’ and ‘standard’ TPhEvent is less than 30%. (Explanation: the main overhead is inside the streamer function). This performance expected to be higher with new disks (they have larger cache).
For shorter events the performance is limited by maximum possible event rate (3300 and 1700 ev/sec)
For longer events the CPU consuming is 3 times less for ‘simple’ TPhEvent.
If we need better performance then the program should be made multithreaded to exploit other CPUs.

## Slide 2: TPhEvent building. Result tables.
Adding subevent, ‘simple’ case:
TPhRawHitTest *pTPhRawHitTest =
new TPhRawHitTest((Int_t*)&(ev->data), (Int_t)ev->bytes/sizeof(long));
pevent->AddObject(pTPhRawHitTest);
--------------------------------------------------------------------
Ev ev/sec KB/sec CPU% CPU% disk disk CPU% CPU%
Size KB EB Gen ev/sec KB/sec EB Gen
--------------------------------------------------------------------
1.2 3393 4126 50% 28% 880 1070 50 3
4 3226 12957 50% 40%
8 2863 22950 46% 48% 549 4403 49 8
10 2410 24146
16 1701 27242 34% 50% 493 7899 47 12
32 873 27973 23% 49%
64 470 30137 17% 50% 128 8215 12% 25%
--------------------------------------------------------------------
Adding subevent, ‘standard’ case:
TPhHashContainer *hash = NULL;
hash = new TPhHashContainer("ZSS");
pevent->AddObject(hash);
for(int ii=0; ii < 8; ii++){
pTPhRawHitTest =
new TPhRawHitTest((Int_t*)&(ev->data), (Int_t)ev->bytes/sizeof(long)/8);
hash->Add((TPhDataObject*)pTPhRawHitTest);}
--------------------------------------------------------------------
Ev ev/sec KB/sec CPU% CPU% disk disk CPU% CPU%
Size KB EB Gen ev/sec KB/sec EB Gen
--------------------------------------------------------------------
1.2 1798 2187 50% 14% 512 623 47 4
4 1758 7062 50% 22%
8 1712 13723 49% 30% 488 3914 47 9
16 1584 25370 50% 46% 367 5878 47 10
64 462 29594 24% 50% 369 8475 30 15

## Slide 3: ROC->EB Data Transfer Rate