## Slide 1: PHOBOS DAQ
Andrei Sukhanov
This presentation will probably involve audience discussion, which will create action items. Use PowerPoint to keep track of these action items during your presentation
In Slide Show, click on the right mouse button
Select “Meeting Minder”
Select the “Action Items” tab
Type in action items as they come up
Click OK to dismiss this box
This will automatically create an Action Item slide at the end of your presentation with your points entered.

## Slide 2: Progress
Done:
  Data taking from whole phobos setup separately
    Sustained data taking rate: 4 MB/sec
  Data transfer to HPSS over gigabit network
    Sustained rate: 10 MB/sec, peak rate: 20 MB/sec
  Communication with data base
  Slow monitoring of silicon parameters

## Slide 3: Attention Areas
Taking data from whole Phobos simultaneously
Low performance of the Ethernet link to silicon
  4 MB/sec, expected 8 MB/sec
Error handling
  Data consistency check
  Lost synchronization between EB and ROC
  Possible loss of data during network transfer
System integrity and stability
  Backup and mirroring
  Phat up to date

## Slide 4: PHOBOS DAQ Hardware
MVME 2306
MVME 2600
MVME 2306
GigaEthernet
to RCF
GigaEthernet
CPU
CPU
CPU
Int Discs
Tape
Fast
Ethernet
Trigger VME
FastEthernet
SUN HPC 3000
LAN
Event Manager
TOF FASTBUS
ADC
TDC
Trig ADC
Trig TDC
SFI
340
RaceWay
RaceWay
RaceWay
RaceWay
Silicon VME
Event Manager
Event Manager

## Slide 5: PHOBOS DAQ Software
Event
Builder
phatdaq.exe
Run Control
(root/phat)
UDP
socket
TCP TSocket
Data & Commands
Data
EB interface
Data taking
ROC:
Length
Seq.number
Command
Source
Type
SubEvent or Command
SubEvent
SubEvent
…
Message:
Length
Event# from Event Manager
Header length
0x12345678
SubEvent:
Data
PhatOnline
Silicon
TOF
Trigger
Run number
Legend:
Working
Structure of the communication messages
Being developed
Work not started yet
ROC
ROC
ROC
Work started
ROCDB
Gateway
Data Base
Slow Monitoring
events

## Slide 6: Synchronization, eng. run
Event
Builder
Silicon
VME
TOF
FASTBUS
Trig
Sync
Data
Handshake and
Commands
Mercury
IOreg
IOreg

## Slide 7: Synchronization, Day 1
Event
Builder
Silicon
VME
TOF
FASTBUS
Data
Handshake and
Commands
Trigger
VME
Setup
Event Manager
Mercury
Mercury
Mercury
Mercury
Mercury
Subevent accepted
Event accepted
Commands
Event#

## Slide 8: Event Manager Interconnections
CI 07
Done1 06
Veto1 05
Trig 1 04
CI 03
CI 02
ExtBusy 01
Trig0 00
PreSc0 12
Scaler0 11
Veto2 09
Trig 2 08
PreSc1 13
PreSc2 14
PreSc3 15
TrigVME ENG.CI
CO 07
CO 06
CO 05
CO 04
CO 03
CO 02
Done 01
Busy 00
TrigPulse 11
StrobCI 10
CO 09
CO 08
PreSc0 13
PreSc1 13
PreSc2 14
ENG.CO
Done2 10
PreSc3 15
CI 07
CI 06
CI 05
CI 04
CI 03
CI 02
CI 01
CI 00
CI 12
CI 11
CI 09
CI 08
MyTrig 13
CI 14
HandShk 15
CO 07
CO 06
CO 05
CO 04
CO 03
CO 02
CO 01
CO 00
CO 11
CO 10
CO 09
CO 08
CO 13
MyTrig 13
Veto 14
ING.CO
CI 10
Ack 15
Plastic ING.CI
CO 07
CO 06
CO 05
CO 04
CO 03
CO 02
CO 01
CO 00
CO 11
CO 10
CO 09
CO 08
CO 13
MyTrig 13
Veto 14
ING.CO
Ack 15
Silicon ING.CI
LED Trigger
- +
- +
- +
- +
- +
- +
CI 07
CI 06
CI 05
CI 04
CI 03
CI 02
CI 01
CI 00
CI 12
CI 11
CI 09
CI 08
MyTrig 13
CI 14
HandShk 15
CI 10

## Slide 9: Schedule
1/31-2/6. More reliable event building
2/7-2/13. Synchronization with event manager in silicon, trigvme
2/14-2/20. Interface between event manager and data base
2/14-2/20. Event selection for online
2/7-2/20. Testing
End of February. System is ready to take data